## Slide 1: Lecture # 5 (Final) Control Logic Design Micro-program, flow-chart, state-diagram

## Slide 2: Introduction
The process of logic design is a complex undertaking.
The data processor part may be general purpose processor unit
The data processor may consist of individual registers and associated digital functions
Fig. 10.1 Control logic and data processor interaction
The control logic initiates all micro-operations in the data processor.
The control logic is a sequential circuit whose internal states dictate the control functions for the system by generating the signals for sequencing the micro-operations.

## Slide 3: Control Organization
Methods of Control Organization
  One flip-flop per state method
  Sequence register and decoder method
  PLA control
  Microprogram control
The first two methods must use SSI and MSI circuits for the implementations.
PLA or microprogram which uses an LSI circuits.

## Slide 4: Microprogram Control
The purpose of the control unit is to initiate a series of sequential steps of microoperations.
A control unit whose control variables are stored in a memory is called a Microprogrammed Control Unit (MCU).
Each control word of memory is called a microinstruction.
A sequence of microinstructions is called a microprogram.

## Slide 5: Hard-wired Control - Example
The design is carried out in five consecutive steps-
  The problem is stated
  An initial equipment configuration is assumed
  An algorithm is formulated
  The data processor part is specified
  The control logic is designed

## Slide 6: 1. Statement of the Problem
Addition and subtraction of binary fixed-point numbers when negative numbers are in sign 2’s complement form.
The addition of two numbers stored in registers of finite length (8 bits) may result in a sum that exceeds the storage capacity of the register by one bit.
The extra bit is said to cause an overflow.

## Slide 7: 2. Equipment Configuration
The two signed binary numbers to be added or subtracted contains n bits.
The magnitudes of numbers contain k = n – 1 bits and are stored in registers A and B.
The sign bits are stored in flip-flops named As and Bs.
Fig. 10-6 Register and associated equipment configuration for the adder-subtractor

## Slide 8: 2. Equipment Configuration
The ALU performs the arithmetic operations, and the 1-bit register E serves as the overflow flip-flop, where the output carry is transferred.
It is assumed that the 2 numbers and their signs have been transferred to their respective registers and that the result of the operation is to be available in registers A and As.
Two input signals in the control logic specify the add (qa) and subtract (qs) operations.
One output variable x indicates the end of the operation.

## Slide 9: 2. Equipment Configuration
The control logic communicates with the outside or external environment through the input and output variables.
Control logic recognizes input signals, qa or qs and provides the required operation.
Upon completion of the operation, the control logic informs the external environment with the output, x that the sum or difference is in registers A and As and the overflow bit is in E.

## Slide 10: 3. Derivation of the Algorithm
When the numbers are added or subtracted algebraically, there are eight different conditions to be considered and may be expressed in compact form as follows:
In the arithmetic operation specified in subtraction, we change the sign of B and add. So, the relationships:
This reduce the number of possible conditions to 4, namely:

## Slide 11: 3. Derivation of the Algorithm contd….
When the signs of A and B are the same, we add the two magnitudes and the sign of the result in the same as the common sign.
When the signs of A and B are not the same, we subtract the smaller number from the larger and the sign of the result is the sign of the larger number.

## Slide 12: Flowchart and state diagram for sign magnitude addition and subtraction operation
Fig. 10-7 Flow chart for sign-magnitude addition and subtraction operation with the equipment of Fig. 10-6

## Slide 13: Explanation of the Flowchart and State Diagram
1. An operation is initiated by either qs or qa inputs
2. Input qs initiates a subtraction operation, so sign of B is complemented
3. Input qa initiates an addition operation, so sign of B is left unchanged
4. Then two signs are compared, As:Bs symbolizes this decision, if two signs are equal then the path marked with = sign is chosen; otherwise, the path marked with ≠ sign is chosen

## Slide 14: Explanation of the Flowchart and State Diagram
5a. If signs are equal then the contents of A is added to the contents of B, and the sum is transferred to A. The value of the end carry is an overflow, as such the E flip-flop is made equal to the output carry, Cout.
5b. If signs are not the same then the contents of B is subtracted from the contents of A, this is done by adding A to the 2's complement of B and the sum is transferred to A. The value of the end carry is zero, that is, there is no overflow, as such the E flip-flop is cleared to zero. However, a 1 in E indicates that A ≥ B, and the number in A is the correct result. The sign of the result again is equal to the original value of As.

## Slide 15: Explanation of the Flowchart and State Diagram
5c. A 0 in E indicates that A < B, then the 2's complement of A is taken and the sign in As is complemented. The 2's complement of A can be done with a micro-operation , where is the 1's complement of A . However, the 2’s complement operation is not available, so it is performed by taking the 1’s complement and then the increment operation, which are available in the designed ALU.
6. Finally, the circuit goes to its initial state and output x is equal to 1 (terminate). If the sign of the result is the same as the original sign of As, the sign bit is left unchanged.

## Slide 16: 4. Data Processor Register
The operations between A and B can be done with the ALU.
The operations with As, Bs and E must be initiated with the separate control variables.
Fig. 10-8 (a) Data Processor Registers and ALU

## Slide 17: 5. Control Block Diagram
The control logic block receives five inputs: two from the external environment and three from the data-processor.
To simplify the design, we define new variable S:
    S = As XOR Bs
Fig. 10-8 (b) Control Logic Block Diagram

## Slide 18: Control State Diagram

## Slide 19: Control State Diagram
Fig. 10-9 (a) State diagram for register transfers

## Slide 20: Control State Diagram
We start by assigning an initial state, T0, to the sequential controller. We then determine the transition to other states T1, T2, T3, and so on.
For each state, we determine the micro-operations that must be initiated by the control logic circuit.
This procedure produces the state diagram for the controller circuit together with a list of register-transfer operations, which are to be initiated while the control logic circuit is in each and every state.

## Slide 21: Sequence of Register Transfers
Fig. 10-9 (b) Sequence of register transfers

## Slide 22: Sequence of Register Transfers
Fig. 10-8 (b) Control Logic Block Diagram
Logic Equations for Hardwired Control Unit Boolean Functions for Output Control

## Slide 23: Sequence of Register Transfers
Logical conjunction (∧)
Logical disjunction (∨)

## Slide 24: Thanks for Attending….
?