## Slide 1: RIP
Course Code: CSC 3116
Dept. of Computer Science
Faculty of Science and Technology
Lecturer No: | Lab 5 | Week No: | 5 | Semester: | 
Lecturer: |  |  |  |  | 
Course Title: Computer Networks

## Slide 2: Lecture Outline
Introduction
Static routing vs dynamic routing
Dynamic routing
Routing information protocol (RIP)

## Slide 3: Introduction
Routing
  routing is the act of forwarding network packets from a source
  network to a destination networks by a router based on its routing table [2].
Fig. A simplified routing table [2]

## Slide 4: Introduction
How is the routing table created?
  Static routing
    If it is done manually by inputting information for each destination network by a network engineer,
    Suitable for very small network
  Dynamic routing
    If the table is created and modified automatically depending on the network condition by a routing protocol
    Dynamic routing can be deployed on small to large size network.

## Slide 5: Dynamic Routing
Features
Facilitates the exchange of routing information between routers
Allow routers to dynamically learn information about remote networks and automatically add this information to their own routing tables
Determines the best path to each network

## Slide 6: Dynamic Routing….
Ways to classify routing protocols
Interior Gateway Protocols or Exterior Gateway protocols
Distance vector or Link state

## Slide 7: Dynamic Routing….
IGP
IGP
  Routing inside an autonomous system (AS), where AS is a collection of network under a common administrator
  Example
    Routing Information Protocol (RIP) version 1
    Interior Gateway Routing Protocol (IGRP)
    Enhanced IGRP (EIGRP)
    Open Shortest Path First (OSPF)
    Intermediate System (IS)-IS

## Slide 8: Dynamic Routing….
EGP
EGP
  Routing between autonomous systems(AS)
  Example
    Border Gateway Protocol (BGP)

## Slide 9: Dynamic Routing….
Classification
Autonomous systems

## Slide 10: Dynamic Routing….
Distance vector routing
Distance vector means that routes are advertised as vectors of distance and direction
Distance is defined in terms of a metric such as hop count, and direction is simply the next hop router or exit interface.
Bellman-Ford algorithm is used for the best-path route determination.
Some distance vector protocols periodically send complete routing tables to all connected neighbors.
In large networks, these routing updates can become enormous, causing significant traffic on the links.
Example
RIP, EIGRP
Distance vector means that routes are advertised as vectors of distance and direction
Distance is defined in terms of a metric such as hop count, and direction is simply the next hop router or exit interface.
Bellman-Ford algorithm is used for the best-path route determination.
Some distance vector protocols periodically send complete routing tables to all connected neighbors.
In large networks, these routing updates can become enormous, causing significant traffic on the links.
Example
RIP, EIGRP
A router communicates with its neighbors only for populating its routing table
Distance vector means that routes are advertised as vectors of distance and direction
Distance is defined in terms of a metric such as hop count, and direction is simply the next hop router or exit interface.
Bellman-Ford algorithm is used for the best-path route determination.
Some distance vector protocols periodically send complete routing tables to all connected neighbors.
In large networks, these routing updates can become enormous, causing significant traffic on the links.
Example
RIP, EIGRP

## Slide 11: Dynamic Routing….
Link state routing
A router configured with a linkstate routing protocol can create a “complete view,” or topology, of the network by gathering information from all the other routers.
A router communicates with all other routers of the network
Only send update (partial) when there is any change in the network topology
Example
OSPF

## Slide 12: Dynamic Routing….
Administrative Distance
The term trustworthiness is commonly used when defining administrative distance.
Administrative distance (AD) defines the preference of a routing source.
Administrative distance is an integer value from 0 to 255.
The lower the value, the more preferred the route source.
An administrative distance of 0 is the most preferred.
Only a directly connected network has an administrative distance of 0, which cannot be changed.

## Slide 13: Dynamic Routing….
Administrative distance

## Slide 14: RIP
Features
  Distance vector routing protocol
  Hop count is used as the metric for path selection.
  If the hop count for a network is greater than 15, RIP cannot supply a route to that network.
  Routing updates are broadcast or multicast every 30 seconds, by default.
  If for some reason, an update for a particular route is not received within a period of 180 seconds then that specific route is declared as invalid and the router which identified that, informs all its neighbors about this invalid route.
  Has two versions: RIPv1 & RIPv2

## Slide 15: RIP
RIP v1-vs-RIPv2
Uses Classless addressing
  RIPv1 uses classful addressing, RIPv2 uses VLSM
Multicasting vs Broadcasting
  Version 1 of RIP uses broadcasting (to 255.255.255.255) to send RIP messages to every neighbor. In this way, all the routers on the network receive the packets, as well as the hosts. RIP version 2, on the other hand, uses the all-router multicast address (224.0.0.9) to send the RIP messages only to RIP routers in the network.
Updates
  RIPv2 sends and receives version 2 updates only. RIPv1 sends version 1 updates and receives both 1 and 2, however version 2 information is ignored.
Authentication
  RIPv2 ensure authentication, while RIPv1 does not

## Slide 16: RIP
Routing table update
Cold Start

## Slide 17: Topic Heading..
Routing table update
Initial Exchange of Information

## Slide 18: Topic Heading..
Routing table update
Table Updating

## Slide 19: Topic Heading..
Routing table update
Next Update

## Slide 20: Topic Heading..
Another Example

## Slide 21: Topic Heading..
New route

## Slide 22: Topic Heading..
Removing a route

## Slide 23: RIPv2 Configuration
172.16.1.0/30
172.16.1.4/30
192.168.2.0/24
IOS Commands
R1(config)# router rip
R1(config-router)# version 2
R1(config-router)#network 172.16.1.0
R1(config-router)#network 172.16.1.4
R1(config-router)#network 192.168.2.0
R1(config-router)#no auto-summary

## Slide 24: RIPv2 Configuration
Trableshooting
172.16.1.0/30
172.16.1.4/30
192.168.2.0/24
To show protocol properties
  show ip protocols
To show all routes
  show ip route
To show all RIP activities in real-time
  debug ip rip
  To stop debugging
  no debug all
  To show RIP database
  show ip rip database

## Slide 25
References
[1] R. Graziani and A. Johnson, Routing Protocols and Concepts, 2nd ed.,
Cisco Systems, Inc., USA, 2008, pp. 148-173.
[2] J. Macfarlane, Network Routing Basics, Wiley Publications. Inc.,
2006, USA, pp. 70-104.

## Slide 26
Books
  1. Official Cert Guide CCNA 200-301 , vol. 1, W. Odom, Cisco Press, First Edition, 2019, USA.
  2. CCNA Routing and Switching, T. Lammle, John Wily & Sons, Second Edition, 2016, USA.